## Slide 1: My Method:
Torque distributor: 100 steps @ 20kHz

## Slide 3: My Method:

## Slide 4: Method in [1] & [2]

## Slide 6
Method in [1] & [2]

## Slide 7: Equal Share

## Slide 9: Equal Share

## Slide 10: To sum up
 | Equal Torque Share | Distribution Prosed in [1] | My Method
Conduction loss (W) (40Nm @ 100RPM) | 76,37 | 76 | 73,24
Torque Ripple (Nm) (40Nm @ 100RPM) | 2,2 | 3,04 | 3,5
Power (W) | 418,88 |  | 
Efficiency (%) | 84,58 | 84,64 | 85,12

## Slide 11: Odaklanılabilecek veya kafamı karıştıran noktalar
Manyetik losslar’a bakılıp fault sonrası durum için kazançlar belki artırılabilir (sağlıklı modülden negatif Id verilip manyetik lossların azaltılması işe yarayabilir, denemek lazım).
Benim hedefim 2 modül ama (for the sake of generality) 4 modül operasyon için Torque Distributor hesaplama olayları karışacak (hesaplama yükü baya bir artacak)
MPC control blockları şuan izoleler birbirlerinden fakat ayrı blokların optimumları ile bütünleşik blokların optimumu farklı olabilir?

## Slide 12: References
[1] Fault-Tolerant Control of Dual Three-Phase Permanent-Magnet Synchronous Machine Drives Under Open-Phase Faults (2019)
[2] Fault Tolerant and Minimum Loss Control of Double-Star Synchronous Machines Under Open Phase Conditions (2008)
[3] Finite Control Set Model Based Predictive Control of a PMSM with Variable Switching Frequency and Torque Ripple Optimization